## Slide 1
Traditional Buildings – Guide to the Application of Building Control and Building Regulations
12th July 2023
Alan Isdell MSCSI MRICS
Pat Nestor MSCSI MRICS
Notes: Introduction
Many thanks for attending today’s session. Volunteerism plays a large part in the society –as you are aware graduates of accredited courses must undertake an assessment of professional competence, and in order for us to be able to provide this we rely solely on the participation of our members to mentor and assess our potential new members.
By being here today you are demonstrating your willingness to help us and the APC candidates engaged in this process and for that we are very grateful.

## Slide 2: Traditional Buildings – Guide to the Application of Building Control and Building Regulations

## Slide 3: Document Status
This document is an ‘Information Paper’
Practice-based information that provides users with the latest technical information, knowledge or common findings from regulatory review.
Information and/or recommended best practice.
Usual principles apply in cases of negligence if technical information is known in the market.

## Slide 4: Why?
Where did the demand for this paper come from.
SCSI Real Cost of Renovation Report
Recommendations for further regulatory guidance in relation to existing buildings
Ongoing deep energy retrofit scheme for existing buildings
From the members working on existing or traditional buildings

## Slide 5: Working Group
Pat Nestor
Alan Isdell
David Humphreys
Brigid Browne
Krystyna Rawicz
Sarah Sherlock
SCSI Member Support Officer - Neil Flannery

## Slide 6: The Key Issues
BCAR
or is it BC(A)R or Building Control (Amendment) Regulations or just Building Control?
Traditional Buildings
High value heritage buildings
Protected structures
Pre 1919, pre 1945 ?
Does a traditional building have to be old?

## Slide 7: Aim of the Information Paper
To assist the practitioner in applying the Building Control Regulations to their project
Focuses on issues commonly arising on traditional buildings
Aims to build familiarity with appropriate application of the Building Control Regulations.

## Slide 8: Mandatory Requirements and Restrictions
The Building Control Regulations are statutory requirements which must be complied with
The role of Assigned Certifier is restricted to Registered Building Surveyors, Registered Architects or Chartered Engineers
Code of Practice for Inspecting and Certifying Buildings and Works
The age or heritage status of a building does not influence whether BCAR applies or not to the works.

## Slide 9: Essential Terms in Building Control
The list in the information paper is not intended to be exhaustive
A 'building' includes part of a building
'Material alterations' is work subject to Part A, B or M.
'Repair or renewal' are works of a routine nature and include returning a building to its original condition. They are not 'material alterations'
'Agriculture', 'guest building', 'flat', 'day centre', 'place of assembly', 'party'
Refer to the definitions in the Act and the Regulations.
'Material change of use' in Building Control differs from Planning

## Slide 10: Giving Notice to Building Control Authority
There are options
7 Day Notice accompanied by a Statutory Declaration and FSC application
Commencement Notice with Accompanying Documentation
Commencement Notice accompanied by Opt-Out Declaration
Commencement Notice without Accompanying Documentation
Differing levels of documentation, control, oversight and certification.

## Slide 11: Design Stage & Final Statutory Certification
7 Day Notice
Commencement Notice with Accompanying Documentation
  Highest level of oversight and professional involvement.
  Design certification, mandatory inspections by the Assigned Certifier,
  Statutory certification by Builder and Assigned Certifier of the works compliance with the requirements of the building regulations.

## Slide 12: No Statutory Certification
Commencement Notice accompanied by Opt-Out Declaration
Commencement Notice without Accompanying Documentation
  The 'Opt-Out'; no statutory design certification, no mandatory professional involvement, no final certification. The homeowner accepts the risks involved by signing the declaration.
  The 'short' commencement notice. No accompanying documents, simple form, no additional certification for design or completion. Small domestic extensions, alterations, shop/office fit-outs

## Slide 13: Essential
Submit the correct form of commencement notice at the correct time
Ensure your client understands the options and implications of the various notices
Some clients may want to opt in

## Slide 14: Do the Building Regulations Apply?
A complex question working with older buildings
Very few projects will be exactly alike
The question should be considered based on the unique merits of each project.
Building Regulations are generally not retrospective
Exceptions; Major Renovations under Part L
Parts G, H & J apply to all new or replacement works
Prohibited to cause a new or greater contravention of building regulations
Works which may harm the fabric of the building are prohibited.

## Slide 15: Structural Changes to a Traditional Building
Significant knowledge and attention to detail required
Many older buildings are fragile and will have reached a structural equilibrium
Building Regulations apply to works which affect the structural integrity of the building or building element being altered or repaired.
Modern inflexible, impermeable materials (steel, concrete) may have a slow but catastrophic impact if inappropriately introduced to an older structure of permeable, flexible materials (timber, lime set masonry).

## Slide 16: Fire Safety
Establish if a Fire Safety Certificate is required or not by reference to the Regulations.
The decision tree flow chart in Appendix A may help build familiarity with this assessment
Material alterations in higher risk buildings such as flats, hotels, hostels, guest buildings or places of assembly will require a FSC
Allow adequate time to design the appropriate options and allow time for the FSC process
Assess the risks
Consider the requirements of the Fire Services Acts 1983 and 2003.

## Slide 17: Every intervention is an opportunity
Improve thermal performance
1
Improve accessibility
2
Improve ventilation
3
Increase the sustainable longevity of the building
4

## Slide 18: Part 4 Building Control Act 1990 Dispensation or relaxation of building regulations
Applications are made to the Building Control Authority
May be appropriate in buildings of high heritage value that are not protected in terms of Part L and obligations around major renovations
Dispensation or relaxation of the functional requirements of the Building Requirements, not a section of a Technical Guidance Document
Significant justification required to convince a Building Control Authority to grant.
A grant may carry conditions and the decision may be appealed

## Slide 19: Finally
Working on traditional buildings requires expertise and experience
Seek further advice where necessary from a Building Conservation Accredited Surveyor or other specialist expert
Understand the long-term impact of the works on the building
Works which damage the fabric of the existing building are prohibited

## Slide 20
www.scsi.ie
Society of Chartered Surveyors Ireland 38 Merrion Square, Dublin 2, Ireland Tel: + 353 (0)1 644 5500 Email: info@scsi.ie
Dating back to 1895, the Society of Chartered Surveyors Ireland is the independent professional body for Chartered Surveyors working and practicing in Ireland. Working in partnership with RICS, the pre-eminent Chartered professional body for the construction, land and property sectors around the world, the Society and RICS act in the public interest: setting and maintaining the highest standards of competence and integrity among the profession; and providing impartial, authoritative advice on key issues for business, society and governments worldwide. Advancing standards in construction, land and property, the Chartered Surveyor professional qualification is the world’s leading qualification when it comes to professional standards. In a world where more and more people, governments, banks and commercial organisations demand greater certainty of professional standards and ethics, attaining the Chartered Surveyor qualification is the recognised mark of property professionalism. Members of the profession are typically employed in the construction, land and property markets through private practice, in central and local government, in state agencies, in academic institutions, in business organisations and in non-governmental organisations. Members’ services are diverse and can include offering strategic advice on the economics, valuation, law, technology, finance and management in all aspects of the construction, land and property industry. All aspects of the profession, from education through to qualification and the continuing maintenance of the highest professional standards are regulated and overseen through the partnership of the Society of Chartered Surveyors Ireland and RICS, in the public interest. This valuable partnership with RICS enables access to a worldwide network of research, experience and advice.